## Slide 1: CSC 1010 Networks & Internet
Network Models
Dr. Mohammed Amine TOGOU
1

## Slide 2: Learning outcomes
• Enumerate the layers of the OSI and TCP/IP models and explain what each layer does
• Give examples of protocols used in each layer
• Describe the concept of data encapsulation
2
CSC 1010: Networks & Internet | Network Models

## Slide 3: Layered communication
3
CSC1010: Networks & Internet | Network models
We use the concept of layers in our daily life, e.g., corresponding through postal mail.
3 actors: a sender, a receiver, and a carrier that transports the letter.
There is a hierarchy of tasks.
Each layer at the sending site uses the services of the layer immediately below it.
The lowest layer uses the services of the carrier.

## Slide 4: Layered communication
4
In networking, we have something similar
We call this setup a layered communication
  The bottom layer is the 0’s and 1’s
  The top layer is the available services
  And there are many layers in-between
CSC1010: Networks & Internet | Network models

## Slide 5: Network communication models
5
  There are two main communication models that you need to know:
    Open Systems Interconnections (OSI)
    TCP/IP
CSC1010: Networks & Internet | Network models

## Slide 6: OSI model
6
It’s theoretical
It’s a blueprint on how to build a network architecture from scratch
It has 7 layers
It defines the services provided by each layer
CSC1010: Networks & Internet | Network models

## Slide 7: Application layer
7
This layer represents the services that directly support applications that use the web: chrome, mobile apps, etc.
It represents the level at which these applications access network services
CSC1010: Networks & Internet | Network models

## Slide 8: Presentation layer
8
It translates data from the Application layer into an intermediary format
It manages security issues by providing services such as data encryption
It compresses data so that fewer bits need to be transferred on the network
CSC1010: Networks & Internet | Network models

## Slide 9: Session layer
9
It allows two applications on different computers to establish, use, and end a session
It establishes dialog control between the two computers in a session
  It regulates which side should transmit, plus when and how long it can transmit
CSC1010: Networks & Internet | Network models

## Slide 10: Transport layer
10
It handles error recognition and recovery for end-to-end communications
It repackages long messages, when necessary, into small parts for transmission
It assembles these parts into the original message at the receiving end
It confirms the receipt of the data through acknowledgments
CSC1010: Networks & Internet | Network models

## Slide 11: Network layer
11
It determines the route from the source to the destination
It manages traffic problems, such as switching, routing, and controlling the congestion of data packets
CSC1010: Networks & Internet | Network models

## Slide 12: Data link layer
12
It packages data from the Network Layer into frames
It transfers frames from one device to another without errors
It waits for an acknowledgment, after sending a frame, from the receiving device
CSC1010: Networks & Internet | Network models

## Slide 13: Physical layer
13
It transmits bits (0s and 1s) from one device to another
It defines how the cable is attached to the network adapter
It specifies what transmission technique is used to send data over the cable
CSC1010: Networks & Internet | Network models

## Slide 14: Data encapsulation/de-encapsulation
14
Each layer adds control information (header) to the user data and pass it to the layer below it
The data link layer adds a header and a trailer
  Trailers are added at the end of the user data to check for errors
At the destination, each layer will remove the header added by the corresponding layer at the source and pass it to the layer above it
CSC1010: Networks & Internet | Network models

## Slide 15: TCP/IP model
15
CSC1010: Networks & Internet | Network models
The practical version of the OSI model
It is the main communication infrastructure supporting the Internet
It has 4 layers
  Few layers in TCP/IP model can provide the services of multiple layers of the OSI model
The name is derived from 2 main protocols: TCP and IP

## Slide 16: OSI vs. TCP/IP
16
CSC1010: Networks & Internet | Network models
OSI
Application
Presentation
Session
Transport
Network
Data Link
Physical
TCP/IP
Application
Network
Access
Transport
Internet

## Slide 17: TCP/IP model
17
CSC1010: Networks & Internet | Network models
Application
Network Access
Transport
Internet
DHCP
DNS
HTTP
TCP
UDP
IP
Ethernet
802.11
Protocol Suite
This is not an exhaustive list. The Application, Internet and Network Access Layers have other protocols.

## Slide 18: Protocols
18
CSC1010: Networks & Internet | Network models
Think of them as a language for machines
They provide a common way for devices to understand each other
They control
Data format
Data content
Timing/synchronisation of communication
Protocols dictate how machines communicate
How the communication is managed

## Slide 19: TCP/IP data encapsulation
19
CSC1010: Networks & Internet | Network models
Application
Network Access
Transport
Internet
User data
User data
HTTP header
User data
App layer header
TCP or UDP header
User data
App layer header
Transp layer header
IP header
User data
App layer header
Transp layer header
IP header
Ethernet header
Ethernet trailer
010011011110011100000011001110100101101110111
PDU
Segment/ Datagram
Packet
Frame

## Slide 20: Addressing
20
CSC1010: Networks & Internet | Network models
Three different levels of addresses are used in the TCP/IP model
  MAC (Media Access Control) addressing at the Network Access layer
  IP addressing at the Internet Layer
  Port addressing at the Transport Layer

## Slide 21: MAC address
21
CSC1010: Networks & Internet | Network models
It is used by the Network Access Layer
The address of the network interface card (NIC) used by device
It is called physical because each NIC has a unique MAC imprinted on it that can never change
  Ethernet uses a 6-bytes (48 bits) MAC address

## Slide 22: IP address
22
CSC1010: Networks & Internet | Network models
It is used by the Internet Layer
It specifies the network, and the hosts connected to it
It is called a logical address because it’s not permanent
No two devices connected to the network/Internet can have the same IP address
It is either 32 or 128 bits long, depending on the Internet Protocol version used

## Slide 23: Port address
23
CSC1010: Networks & Internet | Network models
It is used at the Transport Layer
It identifies processes at the application layer
It is used to know to which process should the data message be delivered to
It is either 2 bytes (16 bits) long

## Slide 24
THANK YOU
CSC 1010: Networks & Internet | Network Models